## Slide 1
SMART INDIA HACKATHON 2026 · SOFTWARE PROTOTYPE TRACK
Problem Statement SIH26038 · Organisation MathWorks · Theme MedTech / HealthTech
Drishti-AI
Explainable dual-stage diabetic retinopathy screening
for rural Primary Health Centres — offline, on the edge, with the AI allowed to abstain.
100%
offline
~1.4 s
end-to-end screening
0%
forced grades on ungradables
99.1%
bandwidth saved
Bezaleel · Madhu · Akshay · Adithya · Sinduri · Megha
Team Lead · Clinical · Deep Learning · Safety · ASHA UX · Clinical UX
Locked to the approved clinical decision flow · Honest scientific guardrails · Built for the last mile, not the lab
Notes: Open with the name, the problem ID, and the one-line thesis: we are not inventing 5-class DR classification — we are making it work in a rural PHC.

## Slide 2
01 — THE CLINICAL REALITY
India cannot screen diabetes-related blindness with specialists alone.
77 million diabetic adults. One ophthalmologist per 100,000 rural citizens. Early triage can save 90% of sight.
77M+
diabetic adults in India
DR is the leading cause of preventable adult blindness.
1 : 100k
rural ophthalmologist ratio
Universal hospital screening is mathematically impossible.
25–35%
ungradable field captures
Handheld, non-mydriatic cameras in camps and PHCs.
70%+
screened eyes are healthy
Without triage, district hospitals drown in false referrals.
The last-mile gap — not a missing model, a missing operating system for rural screening
▸ Community camps, mobile vans, and PHCs use ₹15,000 handheld fundus attachments (Remidio, Forus 3Nethra, Volk iNview) under undilated pupils.
▸ Hospital-lab systems (Google Health ARDA, IDx-DR, EyeArt) proved 5-class grading on Zeiss/Topcon cameras and cloud GPUs. They fail when power, bandwidth, operators, and optics change.
▸ A rural PHC cannot upload 5–15 MB raw images per eye over 2G/3G, cannot wait on cloud GPUs, and cannot staff a retinal specialist on every screening day.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
02 / 15
Notes: Spend 90 seconds here. The number that should land is 1 ophthalmologist per 100,000. Then: the problem is not inventing classification — it is getting screening to run where the patients actually are.

## Slide 3
02 — WHY LABORATORY AI FAILS IN THE FIELD
Four deployment failure modes that a hospital model never sees.
Prior work solved grading under curated conditions. Rural India fails on garbage-in, bandwidth, black-box labels, and specialist overload.
01
Garbage-in, garbage-out
Up to 25–35% of camp captures are motion-blurred, poorly lit, occluded, or not even fundus. A classifier still emits an authoritative grade — missed proliferative disease, or a flood of false referrals.
02
Cloud & bandwidth choke
5–15 MB uncompressed images per eye over 4G/5G is a hospital assumption. Intermittent 2G/3G and power cuts turn cloud inference into camp backlogs.
03
Label without a biomarker
“Grade 2: Moderate NPDR” does not tell a rural physician whether the macula is in danger. Clinicians need macular distance (CSME risk) and visual evidence before spending a referral.
04
District-scale overload
Without local triage, every screened patient is sent onward. Specialists drown in healthy eyes that make up 70%+ of screened populations.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
03 / 15
Notes: The aha: a standard classifier forced to grade every capture is dangerous. That is the failure mode we designed against.

## Slide 4
03 — WHAT WE ARE ACTUALLY BUILDING
We did not invent 5-class DR grading. We operationalised it for rural India.
SIH26038 · MathWorks — last-mile edge screening, not another hospital notebook.
“The AI must know when it cannot answer.”
An ungradable retinal photograph must never be silently forced into a disease prediction. Quality first. Abstention second. Grading only on reliable original pixels.
OUR CONTRIBUTION
● Quality gate before grading, tuned for handheld rural optics
● 100% offline pipeline on a ₹15,000-class laptop CPU
● Quantitative CSME risk from OD–fovea geometry
● District-scale triage that cuts telemetry 99.1%
● Bilingual ASHA workflow + ABDM FHIR reporting
HONEST BOUNDARIES — WHAT WE ARE NOT CLAIMING
○ We did not invent image-quality gating (ARDA, IDx-DR, EyeArt already do it).
○ We are not a certified medical device (CDSCO Class B/C still required).
○ Grad-CAM++ is attention evidence, not automated lesion segmentation.
○ High-risk, low-confidence, and ungradable cases always go to a human.
○ We do not rewrite pixels before Model 2. Original photograph only.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
04 / 15
Notes: This slide wins trust. Judges have seen 50 ‘99% accurate CNN’ decks. Say what we are not claiming, then what we uniquely operationalise.

## Slide 5
04 — FOUR DESIGN QUESTIONS, IN PRIORITY ORDER
Every architecture decision answers one of these. Nothing else.
Sustainability · Availability · Accessibility · Platform independence
01
SUSTAINABILITY
Will it keep running here?
Zero cloud compute bill. Inference on-device. Reject ungradable images before wasting cycles. Designed for existing ₹15k laptops — no forced hardware refresh.
02
AVAILABILITY
Can everyone reach it?
Offline-first screening. Opportunistic sync. 2G/3G packets. 20 PHCs + 5 vans × 100k patients simulated. Specialist load from ~4 doctors down to ~1 tele-reviewer per 100k.
03
ACCESSIBILITY
Can everyone use it?
ASHA/ANM operated. Plain-language recapture. Hindi + English reports, English audio prompts. Commodity cameras. Clear / Review / Urgent at a glance, plus ICDR grades.
04
INDEPENDENCE
Will it run on what they have?
Open-source. Windows, macOS, Linux, Docker. HL7 FHIR R4, SNOMED CT, LOINC, ABDM. Sensor-agnostic: DICOM, JPEG, PNG. No camera SDK lock-in.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
05 / 15
Notes: Walk the four questions in order. Judges should hear that cloud-first was rejected on purpose.

## Slide 6
05 — LOCKED CLINICAL DECISION FLOW
Quality is the first clinical decision. Grading is the second.
Non-destructive. Bounded recapture. Two-tier human review. High-risk always escalates.
1 Capture
Handheld fundus ₹15k attachment
2 Quality
Model 1 gate Good / Mid / Bad
3 Grade
Model 2 · 5-class only if reliable
4 Explain
Grad-CAM++ + CSME distance
5 Act
Report · FHIR refer or recapture
GOOD
Reliable original image → Model 2. Pixel-for-pixel the same photograph that passed the gate. No CLAHE, no sharpening, no generative filters.
BORDERLINE
Reassessment with stricter thresholds. Cleared → Model 2. Still unreliable → treat as Bad. Never silently upgraded.
BAD
Recapture with a specific reason (blur, illumination, FOV). Hard cap of 2 retries, then operator-level human review. DR grade: not generated.
After a reliable grade: confidence check → Grad-CAM heatmap → bilingual PDF + FHIR R4. Low confidence (<60%) or Grade 3/4 → ophthalmologist over-read. Operator review ≠ clinical review.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
06 / 15
Notes: This is the locked flow. Emphasise: Bad images produce ‘DR Prediction: Not generated’. That is the product.

## Slide 7
06 — MODEL 1 · IMAGE QUALITY GATE
Abstain before you grade. Then tell the ASHA worker exactly what to fix.
MathWorks Req 1 · blur · illumination · contrast · FOV · biological defect attribution
WHAT THE GATE MEASURES
Blur / focus
Laplacian variance & multi-scale focus gradients. Motion vs defocus.
Illumination
Underexposure, hotspots, corneal reflection uniformity.
Contrast
Vessel-to-background contrast; ungradable if vessels vanish.
Field of view
Dynamic circular ROI coverage — is enough retina present?
Defect source
Operator error (shake, lid) vs patient pathology (cataract, small pupil).
OPERATOR FEEDBACK
Not “image quality low”.
Actionable, bilingual, audio-capable prompts for ASHA/ANM staff.
“Blur detected — hold the camera steady.”
“Too dark — move closer to the light.”
“Eyelid covering the view — ask the patient to open wide.”
Cap: 2 recaptures, then human review.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
07 / 15
Notes: Demo cue: show a blurry image rejected with a recapture reason. Contrast with a naive classifier that would have graded it.

## Slide 8
07 — MODEL 2, EXPLAINABILITY & BIOMARKERS
Grade only reliable images. Show why. Measure the macula.
MathWorks Req 2–4 · EfficientNetB0 · Grad-CAM++ · OD / fovea / vessels
GRADE 0
No DR
GRADE 1
Mild NPDR
GRADE 2
Moderate
GRADE 3
Severe NPDR
GRADE 4
Proliferative
CLASSIFIER
▸ EfficientNetB0 · 33.4 MB · APTOS 2019
▸ 5-class ICDR severity, referable ≥ Grade 2
▸ ~1.4 s end-to-end on Intel i3 / Ryzen 3, 4 GB RAM
▸ Softmax margin <60% → specialist review
▸ Grade 3 / 4 always flagged, regardless of confidence
GRAD-CAM++
▸ True gradient backprop through final conv maps
▸ Higher-order derivatives for dispersed micro-lesions
▸ <1.2 s on CPU (MathWorks bound: 30 s)
▸ Attention heatmap — not lesion segmentation
▸ Overlaid on the original fundus for audit
STRUCTURE / CSME
▸ Optic disc: intensity + morphological opening
▸ Fovea: macular depression ~2.5 OD diameters temporal
▸ Vessels: top-hat + adaptive Otsu caliber
▸ Euclidean OD–fovea distance → CSME risk
▸ MA / exudate candidates as review overlays
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
08 / 15
Notes: Akshay’s slide. Why EfficientNetB0: parameter-efficient, 33 MB, CPU-real. Why Grad-CAM++: dispersed lesions. Honest: heatmap ≠ segmentation.

## Slide 9
08 — NON-NEGOTIABLE SAFETY RULES (ENFORCED IN CODE)
These are not slideware. They live in the router.
Section 3 / 5 / 7 / 9 / 18 / 20 · two-tier human review
01
Non-destructive processing
No runtime enhancement, CLAHE, sharpening, or generative filters before prediction. The image that reaches Model 2 is pixel-for-pixel the retinal photograph that reached Model 1.
02
Abstention on unreliable images
No Bad or still-unreliable image is handed to Model 2. Output is “DR Prediction: Not generated” plus a specific recapture reason code.
03
Bounded recaptures
Hard cap of 2 recaptures per patient session. Hitting the cap force-escalates to operator-level human review. No infinite retry loops in a camp.
04
Mandatory high-risk override
Grade 3 (Severe NPDR) and Grade 4 (Proliferative DR) are always flagged for ophthalmologist over-read, even at 99% model confidence.
05
Two-tier human review
Operator-level = camera, lighting, recapture. Clinical-level = diagnosis, referral urgency. The system never confuses a bad photo with a bad retina.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
09 / 15
Notes: Read rule 02 and 04 aloud. They are the regulatory posture: human-in-the-loop, abstain-and-escalate, not a diagnostic device claiming autonomy.

## Slide 10
09 — EXPERIMENTAL EVIDENCE
The gate is not a slogan. It changes what patients are told.
150-image A/B/C benchmark · 0% forced prediction on ungradables · full unit + integration suite
METRIC
ARM A · NO GATE
ARM B/C · DRISHTI-AI
WHY IT MATTERS
Forced predictions on ungradable images
100%
0%
No fake grades on blur / garbage
Referable DR specificity (reliable images)
Unreliable
91.6%
Stops flooding district hospitals
Screening recapture / abstention
0% (blind)
20.7%
Bounded field overhead, under 20% target
Human review escalation
0% (silent fail)
75.3%
Ambiguity is surfaced, not buried
Test suites (unit / integration / edge)
—
7 suites, clean
Good / Bad / Borderline paths locked
Arm A is the standard hackathon classifier: 100% of degraded images still receive a clinical-looking grade. Drishti-AI leaks 0%. That is the safety metric we will defend.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
10 / 15
Notes: Adithya’s slide. Lead with 100% vs 0%. Do not oversell the 11.1% sensitivity number from the brief if asked — report CIs honestly and point to the safety metric.

## Slide 11
10 — EXTERNAL VALIDATION · 2,810 REAL LABELED IMAGES
Measured on third-party labeled screening data — nothing copied from a model card.
docs/EVALUATION_RESULTS.md · results/labeled_evaluation.json · python evaluate_labeled_dataset.py
71.5%
TOP-1 ACCURACY
Matches the model card's own 72% APTOS holdout — integration loses nothing.
0.21
REFERABLE-DR SENSITIVITY
Minority recall collapses under domain shift — human review is mandatory, not optional.
6.9%
DOMAIN-GATE FALSE REJECTS
Down from 42% after calibration on real data; over-refuse, never invent.
14 / 14
ADVERSARIAL INPUTS BLOCKED
Faces, documents, screenshots rejected — red-team sweep runs in CI (76 subtests).
QWK 0.31 · macro-F1 0.26 · ECE 0.064
Accuracy is carried by the majority class; these are the honest numbers and we publish them.
Model 1 pass rate: 75.7% (was 40.9%, threshold recalibrated)
Full 2,810-image run; fails safe (over-refuses) and every failure fixture is still rejected.
E2E demo rehearsal: 2/2 runs, 26 assertions green
Boots the real HTTP API: register → risk → quality → analyze → history → adverse input → review queue.
Honest headline: we defend the safety architecture — refuse, defer, escalate — not an accuracy number the model does not have.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
11 / 15
Notes: Lead with the 0.21 sensitivity before a judge finds it. Say: the model is a research baseline (APTOS); everything we built around it — domain gate, quality gate, uncertainty gate, mandatory human review — exists because of exactly this weakness. Every number reproduces with one command: evaluate_labeled_dataset.py.

## Slide 12
11 — DISTRICT-SCALE TELEMEDICINE (MATHWORKS REQ 5)
Filter at the edge. Uplink only what a specialist must see.
MATLAB / Simulink discrete-event queue · 100,000 patients / year · 20 PHCs + 5 vans · 1 district hospital
99.1%
TELEMETRY CUT
439.9 GB raw fundus → 3.8 GB flagged cases + metadata
~4 → ~1
TELE-REVIEWERS / 100K
Specialist bottleneck broken without hiding disease
~1.2 s
ON-SITE TURNAROUND
vs ~1.9 min cloud-only round trip per patient
WHAT THE SIMULINK MODEL ACTUALLY SIMULATES
M/M/c queues
Patient arrivals, edge inference, tele-ophthalmology uplink as a discrete-event system — not a static spreadsheet.
Local processing
Only referable, low-confidence, high-risk, and recapture-exhausted cases leave the PHC.
Capacity proof
Workload drops from 100,000 raw cases to ~16,100 triage cases/year (~62/day) — feasible for a single tele-reviewer.
Hostile networks
Lightweight compressed packets remain viable on intermittent 2G/3G. Screening never waits on the WAN.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
12 / 15
Notes: Akshay/Adithya. 99.1% is the headline. Explain it as ‘we do not upload healthy eyes and ungradable pixels’.

## Slide 13
12 — BUILT FOR THE FIELD, NOT THE DEMO BOOTH
Offline. Commodity hardware. Frontline UX. National digital health rails.
The Flutter app is how judges interact. The product is everything that works outside a hospital.
EDGE & OFFLINE
▸ Zero runtime API calls or weight downloads
▸ Intel i3 / Ryzen 3, 4 GB RAM target
▸ Windows · macOS (Intel & Apple Silicon) · Linux · Docker
▸ One-command judge path: docker compose up
HARDWARE AGNOSTIC
▸ ₹15,000 handheld fundus class (Remidio, Forus, Volk)
▸ No proprietary camera SDK
▸ DICOM / JPEG / PNG ingest
▸ Sensor-agnostic preprocessing
ASHA → DOCTOR UX
▸ Low-cognitive-load recapture HUD
▸ Hindi + English; Tamil/Telugu/Kannada roadmap
▸ Clear / Review / Urgent + ICDR grade
▸ Specialist console: Grad-CAM + CSME overlay
INTEROPERABILITY
▸ HL7 FHIR R4 · SNOMED CT · LOINC
▸ Ayushman Bharat Digital Mission aligned
▸ Bilingual PDF screening dossier
▸ DPDP-aware: no unencrypted PHI on the open WAN
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
13 / 15
Notes: Sinduri/Megha/Bezaleel. Mention bilingual audio for blur. Mention ABDM so it is a national-systems pitch, not a model pitch.

## Slide 14
13 — WHO BUILDS WHAT
Six owners. Seven modules. One locked decision flow.
No orphan components — every module has a named lead and a deliverable.
Bezaleel
TEAM LEAD · FULL-STACK
Decision router, Streamlit, FastAPI, Docker, cross-platform zero-config.
Madhu
CLINICAL LEAD · BIOMED
ICMR 2024 risk engine, OD/fovea CSME distance, clinical report validation.
Akshay
DEEP LEARNING · OPS
EfficientNetB0, Grad-CAM++, MATLAB/Simulink 100k-patient queueing model.
Adithya
SAFETY · VERIFICATION
150-sample benchmark, 0% forced-prediction proof, edge-case hardening.
Sinduri
UX · ASHA FIELD
Mobile workflow, recapture HUD, Hindi audio prompts, Figma system.
Megha
UX · DOCTOR CONSOLE
Tele-ophthalmology workbench, Grad-CAM/CSME overlays, ABDM layouts.
Drishti-AI · SIH26038 · MathWorks · Software Prototype Track
14 / 15
Notes: Introduce in 20 seconds. Do not read bios. Point to live demo owners: Bezaleel (flow), Madhu (clinical), Akshay (model).

## Slide 15
14 — WHAT WE WANT JUDGES TO REMEMBER
We are not building a demo.
We are building the honest, open-source system that lets a validated approach actually reach the people who need it.
Quality first
If the photograph is untrustworthy, there is no grade.
Offline always
A PHC with no internet still finishes the screening.
Humans in the loop
Operator for the camera. Ophthalmologist for the disease.
National rails
FHIR R4 / ABDM — not a walled-garden app.
Drishti-AI
SIH26038 · MathWorks · MedTech · Software Prototype
Bezaleel · Madhu · Akshay · Adithya · Sinduri · Megha
Live app · docker compose up · localhost:8000/app · Q & A
Notes: Close on the manifesto. Invite the demo. Do not reopen architecture. If time: ‘ask us to break it with a bad image.’